Heritage Conservation Briefs

## durability & Energy EFficiency

Durable materials and structural characteristics promote the adaptive reuse of heritage buildings Heritage buildings are inherently energy efficient Easy retrofits can make heritage buildings as energy efficient as most modern buildings

Heritage buildings are durable, and usually

outlive their intended use

A Canadian study examined the age,

structure, and reason for demolition

of  227 buildings with a demolition

permit in a major North American

city.  As the pie chart shows, most

buildings were being demolished for

reasons that were not related to the

structural system or the actual useful

life of the building.  Most buildings

were likely being demolished far

before the end of the useful life of the

structural system.  Only 8 (3.5%) of the

buildings identified a specific problem

with structural or other material or system

as a reason for demolition, 6 of which were older than 75 years.

(The Athena Institute and Forintek Canada Corp., 2004)

#### The old growth wood used in heritage

#### buildings is a superior building material

The wood used in heritage buildings

incorporates both hardwoods and

softwoods often harvested from unfertilized old-growth stock, with a denser and more naturally occurring grain structure than the second-growth stock or fertilized tree farm wood used today.  Such materials out-perform their modern alternatives.  The graph shows that wood as a sole exterior wall material is mostly present in older building stock.  It is generally being replaced by synthetic building materials.

(The Journal of Preservation Technology, 2005 and Natural Resources Canada, 1993 and 1997)

Heritage buildings have inherent energy efficient characteristics

Prior to 1941, buildings were built in a manner consistent with less energy usage for heating and cooling by maximizing the natural source of heating, lighting and ventilation.

### Energy Saving Features of Heritage Buildings

| Feature | How Energy is Conserved |
| --- | --- |
| Operable windows | Provide natural ventilation and light Reduce heat gain or loss since less than 20% of wall is composed of windows |
| Interior light/ventilation courts, Rooftop ventilators, Clerestories, or Skylights | Provide energy efficient fresh air and light |
| Interior or exterior shutters, Interior Venetian blinds, Curtains and drapes, or Exterior awnings | Minimize the heat gain or loss from windows |
| Heavy masonry walls, Thick brick walls, or Stone walls | Minimize heat loss Provide high thermal inertia |

(National Park Service, 1978)

With some upgrades, the energy efficiency of heritage buildings can be increased

Once retrofit components, such as weatherstripping and weatherseals, are incorporated, the energy efficiency of restored windows can meet and even exceed the efficiency of replacement units.

(The Journal of Preservation Technology, 2005)

# Resources

Natural Resources Canada.  1993 and 1997 Survey of Household Energy Use.  Office of Energy Efficiency.

O’Connor, J. 2004. Survey on Actual Service Lives for North American Buildings. Forintek Canada Corp. Found at http://www.durable-wood.com/pdfs/Service_Life_E.pdf.

Sedovic, W. and J.H. Gotthelf. 2005. What Replacement Windows Can’t Replace: The Real Cost of Removing Historic Windows.  APT Bulletin – The Journal of Preservation Technology.  37(4): 25-29.

Smith, B.M. 1978. Preservation Briefs: Conserving Energy in Historic Buildings. National Park Service, Technical Preservation Services.  Found at http://www.cr.nps.gov/hps/tps/briefs/brief03.htm.

The Athena Institute. 2004. Minnesota Demolition Survey: Phase Two Report. Prepared for Forintek Canada Corp. Found at http://www.athenasmi.ca/about/docs/Demolition_Survey.pdf.