|  | MATERIAL SAFETY DATA SHEET |
| --- | --- |

Section 1 - Chemical Product and Company Identification

| MSDS Name: | Alkylbenzene sulfonic acid, mixture of C10-C13 isomers |
| --- | --- |
| Catalog Numbers: | AC325900000, AC325900010, AC325905000 |
| Synonyms: | Mostly dodecylbenzene sulfonic acid. |

| Company Identification: | Acros Organics BVBA Janssen Pharmaceuticalaan 3a 2440 Geel, Belgium |
| --- | --- |
| Company Identification: (USA) | Acros Organics One Reagent Lane Fair Lawn, NJ 07410 |
| For information in the US, call: | 800-ACROS-01 |
| For information in Europe, call: | +32 14 57 52 11 |
| Emergency Number, Europe: | +32 14 57 52 99 |
| Emergency Number US: | 201-796-7100 |
| CHEMTREC Phone Number, US: | 800-424-9300 |
| CHEMTREC Phone Number, Europe: | 703-527-3887 |  |

Section 2 - Composition, Information on Ingredients

| ---------------------------------------- |
| --- |
| CAS#: |  |
| Chemical Name: |  |
| %: |  |
| EINECS#: | unlisted |
| Hazard Symbols: | XN |
| Risk Phrases: |  |
| ---------------------------------------- |  |

Text for R-phrases: see Section 16

| Hazard Symbols: | C |
| --- | --- |
| Risk Phrases: | 22 34 |

Section 3 - Hazards Identification

EMERGENCY OVERVIEW

Danger! Hygroscopic (absorbs moisture from the air). Harmful if swallowed. Causes severe eye and skin burns. Causes severe digestive and respiratory tract burns. Corrosive to metal. Target Organs: Eyes, skin, mucous membranes.

Potential Health Effects

| Eye: | Causes severe eye burns. May cause irreversible eye injury. |
| --- | --- |
| Skin: | Causes severe skin irritation and burns. |
| Ingestion: | Harmful if swallowed. Causes gastrointestinal irritation with nausea, vomiting and diarrhea. May cause burns to the digestive tract. |
| Inhalation: | May cause severe irritation of the respiratory tract with sore throat, coughing, shortness of breath and delayed lung edema. |
| Chronic: | Chronic exposure may cause effects similar to those of acute exposure. |

Section 4 - First Aid Measures

| Eyes: | In case of contact, immediately flush eyes with plenty of water for at least 15 minutes. Get medical aid immediately. |
| --- | --- |
| Skin: | In case of contact, immediately flush skin with plenty of water for at least 15 minutes while removing contaminated clothing and shoes. Get medical aid immediately. Wash clothing before reuse. |
| Ingestion: | If swallowed, do NOT induce vomiting. Get medical aid immediately. If victim is fully conscious, give a cupful of water. Never give anything by mouth to an unconscious person. |
| Inhalation: | If inhaled, remove to fresh air. If not breathing, give artificial respiration. If breathing is difficult, give oxygen. Get medical aid. |
| Notes to Physician: |  |

Section 5 - Fire Fighting Measures

| General Information: | As in any fire, wear a self-contained breathing apparatus in pressure-demand, MSHA/NIOSH (approved or equivalent), and full protective gear. During a fire, irritating and highly toxic gases may be generated by thermal decomposition or combustion. |
| --- | --- |
| Extinguishing Media: | Use extinguishing media most appropriate for the surrounding fire. |
| Autoignition Temperature: | Not available. |
| Flash Point: | > 200 deg C (> 392.00 deg F) |
| Explosion Limits: Lower: | Not available |
| Explosion Limits: Upper: | Not available |
| NFPA Rating: | health: 3; flammability: 1; instability: 0; |

Section 6 - Accidental Release Measures

| General Information: | Use proper personal protective equipment as indicated in Section 8. |
| --- | --- |
| Spills/Leaks: | Absorb spill with inert material (e.g. vermiculite, sand or earth), then place in suitable container. Avoid runoff into storm sewers and ditches which lead to waterways. Provide ventilation. |

Section 7 - Handling and Storage

| Handling: | Wash thoroughly after handling. Remove contaminated clothing and wash before reuse. Use with adequate ventilation. Do not get in eyes, on skin, or on clothing. Keep container tightly closed. Do not ingest or inhale. Do not breathe spray or mist. |
| --- | --- |
| Storage: | Store in a cool, dry place. Keep container closed when not in use. Keep from contact with oxidizing materials. Keep away from metals. Corrosives area. Do not store near alkaline substances. |

Section 8 - Exposure Controls, Personal Protection

| Engineering Controls: |
| --- |
|  | Facilities storing or utilizing this material should be equipped with an eyewash facility and a safety shower. Use process enclosure, local exhaust ventilation, or other engineering controls to control airborne levels. |
| Exposure Limits+--------------------+-------------------+-------------------+-----------------+ ¦ Chemical Name ¦ ACGIH ¦ NIOSH ¦OSHA - Final PELs¦ ¦--------------------¦-------------------¦-------------------¦-----------------¦ ¦ ¦none listed ¦none listed ¦none listed ¦ ¦--------------------¦-------------------¦-------------------¦-----------------¦ ¦ Dodecylbenzenesulfo¦none listed ¦none listed ¦none listed ¦ ¦ nic acid ¦ ¦ ¦ ¦ ¦--------------------¦-------------------¦-------------------¦-----------------¦ ¦ Benzenesulfonic aci¦none listed ¦none listed ¦none listed ¦ ¦ d, 4-C10-13-sec-alk¦ ¦ ¦ ¦ ¦ yl derivitives ¦ ¦ ¦ ¦ +--------------------+-------------------+-------------------+-----------------+ OSHA Vacated PELs: : None listed Dodecylbenzenesulfonic acid: None listed Benzenesulfonic acid, 4-C10-13-sec-alkyl derivitives: None listed |

| Personal Protective Equipment |
| --- |
| Eyes: | Wear chemical splash goggles. |
| Skin: | Wear appropriate gloves to prevent skin exposure. |
| Clothing: | Wear appropriate protective clothing to prevent skin exposure. |
| Respirators: | A respiratory protection program that meets OSHA's 29 CFR 1910.134 and ANSI Z88.2 requirements or European Standard EN 149 must be followed whenever workplace conditions warrant respirator use. |

Section 9 - Physical and Chemical Properties

| Physical State: | Viscous liquid |
| --- | --- |
| Color: | brown |
| Odor: | sulfur dioxide odor |
| pH: | Not available |
| Vapor Pressure: | Not available |
| Vapor Density: | Not available |
| Evaporation Rate: | Not available |
| Viscosity: | Not available |
| Boiling Point: | 315 deg C @ 760 mmHg ( 599.00°F) |
| Freezing/Melting Point: | 10 deg C ( 50.00°F) |
| Decomposition Temperature: | Not available |
| Solubility in water: | Soluble |
| Specific Gravity/Density: | 1.2000 |
| Molecular Formula: | C18H30O3S |
| Molecular Weight: | 322.00 |

Section 10 - Stability and Reactivity

| Chemical Stability: | Stable under normal temperatures and pressures. |
| --- | --- |
| Conditions to Avoid: | Excess heat. |
| Incompatibilities with Other Materials | Metals, strong oxidizing agents, strong bases, Corrosive to steel and aluminum.. |
| Hazardous Decomposition Products | Carbon monoxide, oxides of sulfur, carbon dioxide. |
| Hazardous Polymerization | Will not occur. |

Section 11 - Toxicological Information

| RTECS#: | CAS# : None listed CAS# 27176-87-0: DB6600000 CAS# 85536-14-7: None listed |
| --- | --- |
| LD50/LC50: | RTECS: Not available. RTECS: CAS# 27176-87-0: Oral, rat: LD50 = 650 mg/kg; . RTECS: CAS# 85536-14-7:. |
| Carcinogenicity: | - Not listed as a carcinogen by ACGIH, IARC, NTP, or CA Prop 65. Dodecylbenzenesulfonic acid - Not listed as a carcinogen by ACGIH, IARC, NTP, or CA Prop 65. Benzenesulfonic acid, 4-C10-13-sec-alkyl derivitives - Not listed as a carcinogen by ACGIH, IARC, NTP, or CA Prop 65. |
| Epidemiology: | Not available |
| Teratogenicity: | Not available |
| Reproductive: | Not available |
| Neurotoxicity: | Not available |
| Mutagenicity: | Not available |
| Other: | Not available |

Section 12 - Ecological Information

| Ecotoxicity: | Fish: Rainbow trout: LC50 = 10.8 mg/L; 96 Hr.; Static conditions Water flea Daphnia: EC50 = 11-23 mg/L; 48 Hr.; Unspecified |
| --- | --- |

Section 13 - Disposal Considerations

Chemical waste generators must determine whether a discarded chemical is classified as a hazardous waste. US EPA guidelines for the classification determination are listed in 40 CFR Parts 261.3. Additionally, waste generators must consult state and local hazardous waste regulations to ensure complete and accurate classification. RCRA P-Series: None listed. RCRA U-Series: None listed.

Section 14 - Transport Information

US DOT

Shipping Name: ALKYL SULFONIC ACIDS, LIQUID

Hazard Class: 8

UN Number: UN2586

Packing Group: III

Canada TDG

Shipping Name: Not available

Hazard Class:

UN Number:

Packing Group:

USA RQ: CAS# 27176-87-0: 1000 lb final RQ; 454 kg final RQ

Section 15 - Regulatory Information

US Federal

TSCA CAS# is not listed on the TSCA Inventory. It is for research and development use only. CAS# 27176-87-0 is listed on the TSCA Inventory. CAS# 85536-14-7 is listed on the TSCA Inventory.

| Health & Safety Reporting List | None of the chemicals are on the Health & Safety Reporting List. |
| --- | --- |
| Chemical Test Rules | None of the chemicals in this product are under a Chemical Test Rule. |
| Section 12b | None of the chemicals are listed under TSCA Section 12b. |
| TSCA Significant New Use Rule | None of the chemicals in this material have a SNUR under TSCA. |
| CERCLA Hazardous Substances and corresponding RQs | CAS# 27176-87-0: 1000 lb final RQ; 454 kg final RQ |
| SARA Section 302 Extremely Hazardous Substances | None of the chemicals in this product have a TPQ. |
| Section 313 | No chemicals are reportable under Section 313. |
| Clean Air Act: | This material does not contain any hazardous air pollutants. This material does not contain any Class 1 Ozone depletors. This material does not contain any Class 2 Ozone depletors. |
| Clean Water Act: | CAS# 27176-87-0 is listed as a Hazardous Substance under the CWA. None of the chemicals in this product are listed as Priority Pollutants under the CWA. None of the chemicals in this product are listed as Toxic Pollutants under the CWA. |
| OSHA: |  |
| STATE | is not present on state lists from CA, PA, MN, MA, FL, or NJ. Dodecylbenzenesulfonic acid can be found on the following state right to know lists: California, New Jersey, Pennsylvania, Massachusetts. Benzenesulfonic acid, 4-C10-13-sec-alkyl derivitives is not present on state lists from CA, PA, MN, MA, FL, or NJ. |
| California Prop 65 |  |
| California No Significant Risk Level: | None of the chemicals in this product are listed. |

European/International Regulations

European Labeling in Accordance with EC Directives Hazard Symbols: C Risk Phrases: R 22 Harmful if swallowed. R 34 Causes burns. Safety Phrases: S 26 In case of contact with eyes, rinse immediately with plenty of water and seek medical advice. S 28A After contact with skin, wash immediately with plenty of water. S 36/37/39 Wear suitable protective clothing, gloves and eye/face protection. WGK (Water Danger/Protection) CAS# : Not available CAS# 27176-87-0: Not available CAS# 85536-14-7: 2 Canada CAS# 27176-87-0 is listed on Canada's DSL List CAS# 85536-14-7 is listed on Canada's DSL List Canadian WHMIS Classifications: E This product has been classified in accordance with the hazard criteria of the Controlled Products Regulations and the MSDS contains all of the information required by those regulations. CAS# is not listed on Canada's Ingredient Disclosure List. CAS# 27176-87-0 is listed on Canada's Ingredient Disclosure List CAS# 85536-14-7 is not listed on Canada's Ingredient Disclosure List.

Section 16 - Other Information

| MSDS Creation Date: | 9/25/1997 |
| --- | --- |
| Revision #5 Date | 3/18/2004 |

The information above is believed to be accurate and represents the best information currently available to us. However, we make no warranty of merchantibility or any other warranty, express or implied, with respect to such information, and we assume no liability resulting from its use. Users should make their own investigations to determine the suitability of the information for their particular purposes. In no event shall the company be liable for any claims, losses, or damages of any third party or for lost profits or any special, indirect, incidental, consequential, or exemplary damages howsoever arising, even if the company has been advised of the possibility of such damages.