SAFETY DATA SHEET

## SECTION 1. PRODUCT AND COMPANY IDENTIFICATION

MANUFACTURER: TRANSENE COMPANY, INC.

# ADDRESS: DANVERS INDUSTRIAL PARK

# 10 ELECTRONICS AVENUE DANVERS, MA 01923,

# TEL: (978) 777-7860 FAX: (978)-739-5640

# WWW.TRANSENE.COM

#### EMERGENCY NO. 1-800-424-9300 CHEMTREC

| MATERIAL NAME: TRANSENE SULFITE GOLD TSG-250 REVISED: April 2016 CHEMICAL FAMILY: Gold Sulfite Solution Product Number: 110-TSG-250 |
| --- |
| SECTION 2. HEALTH HAZARD INFORMATION GHS Classifications H303: Acute toxicity Oral : Category 5 H333: Acute toxicity Inhalation : Category 5 H316: Skin corrosion / Skin irritation : Category 3 H319: Serious eye damage / Eye irritation : Category 2A Pictograms or Hazard symbols |  |  |
| Warning: Causes eye irritation. Warning: Causes mild skin irritation. May be harmful if swallowed, inhaled, or in contact with skin. Precautionary Statements P264 Wash thoroughly after handling. P280 Wear protective gloves, clothing, and eye and face protection. P304 + P312 If inhaled, call a physician if you feel unwell. P305 + P351 + P338 If in eyes, rinse cautiously with water for several minutes. P332 + P313 If skin irritation occurs, get medical advice/attention. P337 + P313 If eye irritation persists, get medical advice/attention. |  |  |

###### SECTION 3.COMPOSITION/INFORMATION ON INGREDIENTS

| Material Sodium Gold Sulfite CAS# 19153-98-1 Sodium Sulfite CAS# 7757-83-7 Water CAS# 7732-18-5 Total | Wt % 1-5 1-5 > 90 100 | Toxicity |
| --- | --- | --- |

SECTION 4. FIRST AID MEASURES

#### EFFECTS OF OVEREXPOSURE

FIRST AID:

EYES: Immediately flush with large quantities of water for at least 15 minutes and call a physician.

SKIN: Flush with large amounts of water for at least 15 minutes.  Wash with soap and water.  Remove 	contaminated clothing.

INGESTION: If conscious, immediately give 2-4 glasses of water or milk and induce vomiting.  Seek 	immediate medical attention by physician.

INHALATION: Remove victim to fresh air.  Seek medical attention.

Caution: If unconscious - having trouble breathing - or in convulsions do not induce vomiting or give water.

Always clean contaminated clothing and gear prior to reuse. NEVER administer anything to an unconscious 	person.

Overexposure to mist can cause tissue damage, especially to eyes and lungs.

| SECTION 5. FIRE FIGHTING MEASURES |
| --- |
| Flash Point and Method non-flammable | Autoignition Temp. NA | Flammability Limits In Air | LOWER NA | UPPER NA |

Extinguishing media: Water spray or fog, carbon dioxide and dry chemical.

Special fire fighting procedures: None

SECTION 6. ACCIDENTAL RELEASE MEASURES

SPILLS, LEAKS: Ventilate area of leak or spill. Dike and cover the contaminated areas with absorbent, non-combustible material such as earth, sand, or vermiculite.

#### SECTION 7. HANDLING AND STORAGE

Wash thoroughly after handling.  Remove contaminated clothing and wash before re-use.  Do not breathe mist or vapor.  Do not expose eyes, skin, or clothing.  Keep container closed tightly.  Use with adequate ventilation or respiratory protection. Do not store near combustibles or in direct sunlight.  Store in a cool, dry, well-ventilated area away from incompatible substances.  Separate from strong acids.

SECTION 8. EXPOSURE CONTROL/PERSONAL PROTECTION

Respiratory protection: None required.

Ventilation:	Where adequate ventilation is not available, use NIOSH approved vapor respirator with dust, fume and mist filters. Local ventilation through fume hoods or laminar flow stations is also preferred. Keep fumes away from strong bases.

Protective gloves: Skin contact should be minimized through use of rubber gloves.

Other protective equipment:	Steel tipped shoes/eye wash station/chemical safety chemical retardant clothing.  Eye protection: Safety goggles / face shield

SECTION 9. PHYSICAL AND CHEMICAL PROPERTIES

Form :								  Liquid

Appearance :                                                                           Colorless to light yellow

Odor :                                                                 None

pH :                                                                                          6.9-7.3

Melting point:                                                                          0 oC

Boiling point/Boiling range :                                                 100 oC (water)

Flash point :                                                                             Non-flammable.

Ignition point :                                                                         Will not ignite.

Danger of explosion:                                                               Product is not explosive

Vapor density (Air = 1) :                                                        Not available

Volatiles, %:                                                                            > 98

Vapor pressure at 15o C, mm Hg:                                         Not available

Specific gravity :                                                                     1.08 g/cc

Solubility in / Miscibility:                                                       Completely miscible in water

Evap. Rate (Water = 1):                                                          > 1

##### SECTION 10.  STABILITY AND REACTIVITY

| Stability | Stable X Conditions to avoid: Excess heat , light, confined spaces Unstable |
| --- | --- |
| Incompatible with: Strong acids; oxidizers Hazardous decomposition products: Carbon and carbon oxides; ammonia |
| Hazardous polymerization: | May occur Conditions to avoid: Excess heat, damp. Will not occur X |

SECTION 11. TOXICOLOGICAL INFORMATION EYES: Immediately flush with large quantities of water for at least 15 minutes and call a Physician. SKIN: Flush with large amounts of water for at least 15 minutes. Wash with soap and waterwater. Remove contaminated clothing. INGESTION: If conscious, immediately give 2-4 glasses of water or milk and induce vomivomiting. Seek immediate medical attention by physician. INHALATION: Remove victim to fresh air. Seek medical attention. Caution: If unconscious - having trouble breathing - or in convulsions do not induce vomivomiting or give water. AlwaAlways clean contaminated clothing and gear prior to reuse. NEVER administer anything to an unconscious person. SECTION 12. ECOLOGICAL INFORMATION Bioaccumulation : There is no evidence of bioaccumulation. Ecotoxicity : Biologic effects: No data for this product. SECTION 13. DISPOSAL CONSIDERATIONS DISPOSAL: Dispose of in accordance with all federal state and local regulations. Send waste to an approved waste disposal facility. SECTION 14. TRANSPORTATION INFORMATION Non-hazardous/non-regulated. SECTION 15. REGULATORY Symbol: C, Corrosive R-Phrase: R21/22: Harmful in contact with skin and if swallowed. S-Phrases: S17: Keep away from combustible material. SECTION 16. OTHER INFORMATION NFPA Codes: Health: 1 Flammability: 0 Reactivity: 0 All ingredients of this product are listed on the US TSCA inventory under their parent anhydrous compounds.