## Slide 1: I- or G-optimal: Do We Have To Choose?
Stephen J. Walsh1, Lu Lu2, and Christine Anderson-Cook3
Joint Research Conference 2024: Data Science and Statistics for Industrial Innovation
Quality Engineering Invited Session
June 17 – 20, 2024
Waterloo, Ontario, Canada
1 Utah State University Department of Mathematics and Statistics
2 University of Southern Florida Department of Mathematics and Statistics
3 Los Alamos, NM

## Slide 2: Outline
Optimal Design Notation and Definitions
Overview of G- and I-optimal design research and current practices
Multi-objective optimal design: the search for the Pareto Front
Case study Examples:
  Generating the Pareto Front Candidate
  Analyzing Pareto Front Design Candidates and Identifying ‘good’ Designs
Publication Summary: design scenarios covered and accessing Pareto Front Optimal G/I Tradeoff Designs
Conclusions

## Slide 3: 1. Optimal Design Notation and Definitions

## Slide 4: In this presentation we consider:
Exact (as opposed to continuous optimal designs for small response surface methodology (RSM) scenarios.
Designs for the second-order model
K = 1, 2, 3, and 4 experimental factors, several N (number of experimental runs)
Design point Design Space
Second-order model in factors
Exact Design Matrix, K = 3 Factors
Model Expansion Vector
Full Linear Model (post experiment regression fitting)

## Slide 5: Framing the optimal DoE problem: uncertainty attributable to the experiment
Total Model Information Matrix
Parameter estimation and uncertainty quantification
Space of Candidate Design Matrices
Dimension =
choose a ‘good’ design from this space of candidates
Prediction Variance Criteria
Coefficient Precision Criteria

## Slide 6: Constructing an Optimal Design
Optimal Designs are Defined As:
Which are optimizations of non-convex (multimodal) objectives on dimensional search spaces
Comments on Generating Exact G/I-optimal designs
(as opposed to continuous designs) there is no theory on which to verify that a candidate design is optimal, thus:
  candidate optimal designs are generated computationally via some optimization algorithm,
  recent literature consists of studies that publish results under a specific algorithm as well as their best designs.
No Free Lunch in Optimization (Wolpert and Macready 1997)
  no ‘best’ optimization algorithm across all design scenarios (model, n, criterion),
  i.e. some optimization algorithms may be more efficacious to a specific optimal design problem then others…
More on algorithms later…
Given candidate design ,
Find its max prediction variance
Search space of candidate matrices for optimal design

## Slide 7: 2. Overview of G- and I-optimal design research and current practices

## Slide 8: G- vs. I-optimal Designs in Research
1918
Kirstine Smith, 1918, Biometrika
Considered the first paper on optimal design concept
1950s
Theory of optimal design for continuous (measure theoretic) designs
e.g. Kiefer, 1959 and others.
2003
Borkowski, 2003, Journal of Probability and Statistical Science
Used a Genetic Algorithm to Generate Exact Optimal Design Candidates for
G-optimal designs supporting a 1st up to 6-order polynomial model for K = 1 factors
D-, A-, G-, I-criteria
K = 1, 2, 3 experimental factors, seven design sizes N per K, second order model.
General Equivalence Theorem
Highly cited: used by researchers as a benchmark and validation dataset for assessing algorithm efficacy

## Slide 9: G- vs. I-optimal Designs in Research
2010
Rodriguez, Jones, Borror, Montgomery, 2010, Journal of Quality Technology
2015
Saleh and Pan, 2015, Journal of Statistical Computation and Simulation
2018
Hernandez and Nachtsheim, 2018, Technometrics
Generated D-, I-, G-optimal designs via coordinate exchange
Reproduced designs proposed by Borkowski, 2003
Extended to K = 4, 5 factor cases
Studied prediction variance properties of the G- and I-optimal designs.
Modified coordinate exchange with clustering to generate G-optimal designs
Reproduced designs proposed by Borkowski, 2003
Exploited weighted continuous I-optimal designs as starting point for coordinate exchange and G-optimal design search
Fast algorithm to generate highly efficient G-optimal designs
Proposed designs for two new K = 4, 5 experimental factor scenarios
Recommend practitioners pursue I-optimal designs for ease of computation and prediction variance properties.

## Slide 10: G- vs. I-optimal Designs in Research
2022
Walsh and Borkowski, 2022, Mathematics
2023
Walsh, Lu, and Anderson-Cook, 2023, Quality Engineering
Adapted particle swarm optimization (PSO) to generate G-optimal designs
(sometimes significantly) improved G-optimal designs found for many K = 2, 3, 4, 5 factor cases
Same cost as algorithm proposed by Hernandez and Nachtsheim, 2018, but higher probability of generating highly efficient designs.
PSO thus demonstrated to be state-of-the-art algorithm for working with the G-criteria.
Revisit the study of G/I-optimal design tradeoffs as in Rodriguez et. al., 2010.
More thorough investigation via multi-objective optimal designs
Several design scenarios are found to have designs that are highly efficient on both the G- and I-criteria

## Slide 11: Examples and Fraction of Design Space (FDS) Plot
Scaled Prediction Variance of each design over study space
FDS plot proposed by Alyaa (Zahran) Abdelaziz et. al. (2003, Journal of Quality Technology)
Based on such results, Rodriguez, Jones, Borror, and Montgomery, 2010 observed and recommended:
  It is immensely easier and cheaper to generate highly efficient I-optimal designs (as opposed to G-optimal designs)
  I-optimal designs exhibit lower SPV at large proportions of design space, thus should be preferred

## Slide 12: Summary
Generating exact G-optimal designs is:
  Difficult and (relatively) computationally expensive.
  Prone to error.
  Borkowski (2003), Rodriquez et. al. (2010), Hernandez and Nachtsheim (2018), Saleh and Pan (2015)Walsh and Borkowski (2022).
Generating I-optimal designs:
  Cheaper and less prone to error (timescale probably tolerable by practitioners).
  Exhibit lower prediction variance than G-optimal designs on ~80% of design space.
  G-optimal designs often sacrifice good I-efficiency, and vise-versa.
Therefore, Rodriquez et. al. (2010) suggest I-optimal designs should be preferred.
Do there exist designs that retain properties of both G- and I-optimal designs?

## Slide 13: 3. Multi-objective optimal design: the search for the Pareto Front

## Slide 14: Pareto Front Optimal Design
Experimental objective is now multivariate
The optimal design problem is formulated as
Defining an optimal design in this context now requires
User specified desirability – info not contained in above expression
Definition of Pareto Front: the set of non-dominated solutions

## Slide 15: Conceptual: Optimal design for Objectives
Feasible Region:
-dimensional Hypercube
Space of Candidate Designs
Image of Feasible Region in Objective Space
Ideal Point
Utopia Region
Non-dominated
Solutions: Pareto Front
The computing goal is now to:
Find the designs in the feasible region that exist
on the Pareto Frontier of the image of the
feasible designs in multi-objective space.

## Slide 16: Desirability Metrics
For the multivariate optimization problem
With ideal point
The weighted -norm is
Define translated criterion vector
Specific metrics
Additive Desirability
Euclidean Distance
Tchebytchev Desirability

## Slide 17: The multi-objective optimal design problem
Computing goal is (for a range of preference weights)
PSO is run several hundred times per weight (global optimum not guaranteed)
From set of candidate solutions, extract the non-dominated solutions
  This is the candidate/propose Pareto Front Design
Post-hoc analysis elucidates properties and tradeoffs

## Slide 18: 4. Case Study Examples

## Slide 19: Summary
Illustrate PF construction and analysis process for design scenario
  K = 2, N = 9
Range of weights explored
Hundreds of optimization runs per weight
Thousands of optimization runs per scenario
Yields approximation of Pareto Front
Contains hundreds to thousands of optimal designs
Further analysis required
Extract a manageable set of representative optimal designs over all desirability
Explore implications and tradeoffs of optimal designs under different desirability's
The implemented design is more consistent with the practitioner's requirements.
Statistician informs collaborator of design candidates and properties
Esp. the tradeoffs of the designs and implications for desirability
Optimize Desirability
Extract Non-Dominated Solutions
Thin a Dense Pareto Front and Analyze
Communication
(In Practice) Select a Design
Design Construction: Computing and Analysis
Collaboration
Implementation

## Slide 20: K = 2, N = 9, Second Order Model
Optimize Additive Desirability
Extract Pareto Front and Representative Designs
Summarize PV Properties of Representative Designs
PSO parameters:
G/I-criterion runs: 500 PSO runs, 300 particles, local communication topology.
Desirability runs: 200 PSO runs,50 particles, global communication topology
  (50 values)
11,000 PSO optimization runs for this design scenario
Pareto Front Identification and Design Extraction:
Grey Points: extraction of Pareto Front candidates via set definition
Colored points: sub-selection of designs from dense pareto front aided by epsilon-dominance algorithm
Note yellow designs G- and I-relative efficiency.
Analyze Design Properties 1:
FDS profiles of colored designs
Yellow design has high relative G-efficiency and an FDS profile more similar to the I-optimal design.

## Slide 21: K = 2, N = 9, Second Order Model: Analyze Design Properties 2
Select those that are optimal on
Additive desirability
Tradeoff plot:
G and I-efficiencies of PF designs
Synthesized efficiency plot:
Relative performance of design vs. best over all possible weights.
5502 , which is optimal for w = 0.5, is at least 95% efficient (white) for a wide range of weights from 0.2 to close to 0.7
Design extraction via epsilon dominance algorithm

## Slide 22: Representative Designs
FDS Profiles
The G- or I-optimal designs pay a steep efficiency price on the other criteria (blue and green)
Designs that tend to simultaneously optimize additive desirability of both criteria require approximately 80% preference toward the I-criteria (20% preference to G-).
The yellow design optimizes both, gives high efficiency on each criteria, and incidentally appears to be the FC-CCD for this design scenario
Selected Pareto Front Designs

## Slide 23: 5. Publication Summary: design scenarios covered and accessing Pareto Front Optimal G/I Tradeoff Designs

## Slide 24: A Pareto Front Optimal Design Catalog for Small Exact Optimal Design Scenarios
Provide exposition of Multi-Objective Optimal Design Concept and all Technical and Computational Procedures
Provide a large catalog of Pareto Front Candidates for
  (seven scenarios) K = 2 experimental factors, N = 6, 7, …, 12 run sizes
  (seven scenarios) K = 3 experimental factors, N = 10, 11, …, 16 run sizes
  (three scenarios) K = 4 experimental factors, N = 15, 17, 20 run sizes
https://www.tandfonline.com/doi/full/10.1080/08982112.2023.2194963
Google Scholar: 8 citations as of 6/13/2024
A total 13,333 designs are available. Generated under nearly 200,000 optimization searches

## Slide 25: Data Structure: K = 2, N = 6
R-script is provided to run the epsilon-dominance extraction algorithm for subsetting this dense Pareto Front into a set of representative designs
User can apply their own desirability function if needed.
An R-function is provided to parse the Designs (column F) into an R-matrix object.

## Slide 26: K = 2 Factor Findings
For some design scenarios, we found that the Pareto Frontier is convex toward the utopia point
  There exist designs that achieve high efficiency on both criteria
For other scenarios, there do not exist designs highly efficient on both criteria

## Slide 27: K = 3 Factor Findings
K = 3, N = 12: there exists a design 90% efficient on both criteria
K = 3, N = 10: no design that performs well on both criteria
K = 3, N = 14:
  Gap in Pareto Front
  Designs with high I-efficiency have low G-efficiency, – but –
  Designs with high G-efficiency have high I-efficiency

## Slide 28: K = 4 Factor Findings
Significant computational burden in higher dimensions
Opportunities for improving computing approach
Initial proposal at Pareto Fronts for these cases
Can be used as benchmarking dataset for computing improvements
Design size | I-optimal (Blue) | Red | Purple | Orange | G-optimal (Green)
15 | (100,52.1) | (96.6,69.9) | (90.4,83.0) | (82.9,97.2) | (69.4,100)
17 | (100,69.8) | (97.9,78.9) | (91.7,92.3) | (74.7,97.4) | (61.1,100)
20 | (100,64.4) | (95.6,81.9) | (89.5,93.8) | (85.9,98.7) | (68.4,100)
Summary of performance for five selected designs in Figures 9 and 10 for K=4 and N=15, 17, and 20.
The results shown are (I-efficiency, relative G-efficiency)

## Slide 29: 6. Conclusions

## Slide 30: Conclusions
Pareto Front Optimal Design is a relatively new concept in experimental design.
First instance of honoring continuous design space (flexibility of meta-heuristic optimization algorithms such as PSO).
G-crit optimal design itself is hard. Conventional wisdom is that I-optimal designs are easier to compute and always better.
  We learned, not always!
  There exist, for some scenarios, designs that achieve good efficiency on both G- and I-criteria
Our large database of Multi-Objective optimal designs is available to practitioners and can serve as a benchmark dataset for developing algorithms to solve this problem more efficiently

## Slide 31: References
D. H. Wolpert and W. G. Macready, "No free lunch theorems for optimization," in IEEE Transactions on Evolutionary Computation, vol. 1, no. 1, pp. 67-82, April 1997, doi: 10.1109/4235.585893.
KIRSTINE SMITH, ON THE STANDARD DEVIATIONS OF ADJUSTED AND INTERPOLATED VALUES OF AN OBSERVED POLYNOMIAL FUNCTION AND ITS CONSTANTS AND THE GUIDANCE THEY GIVE TOWARDS A PROPER CHOICE OF THE DISTRIBUTION OF OBSERVATIONS, Biometrika, Volume 12, Issue 1-2, November 1918, Pages 1–85, https://doi.org/10.1093/biomet/12.1-2.1
J. Borkowski. “Using a genetic algorithm to generate small exact response surface designs.” Journal of Probability and Statistical Science, 1(1), Feb. 2003.
M. Rodriguez, B. Jones, C. M. Borror, and D. C. Montgomery. "Generating and assessing exact G-optimal designs.” Journal of Quality Technology, 42(1):3-20, 2010.
Saleh, M., & Pan, R. (2015). A clustering-based coordinate exchange algorithm for generating G-optimal experimental designs. Journal of Statistical Computation and Simulation, 86(8), 1582–1604. https://doi.org/10.1080/00949655.2015.1077252
Hernandez L.N. and Nachtsheim, C. J. “Fast computation of exact G-optimal designs via Il-optimality”. Technometrics, 60(3):297-305, 2018.
Lu, L., Anderson-Cook, C.M. (2013), “Adapting the Hypervolume Quality Indicator to Quantify Trade-offs and Search Efficiency for Multiple Criteria Decision-making using Pareto Fronts”, Quality and Reliability Engineering International, 29, 1117-1133.
Lu, L., Anderson-Cook, C.M. (2014), “Balancing Multiple Criteria Incorporating Cost Using Pareto Front Optimization for Split-Plot Designed Experiments”, Quality and Reliability Engineering International, 30, 37-55.
Lu, L., Anderson-Cook, C.M., Lin, D. (2014) “Optimal Designed Experiments Using a Pareto Front Search for Focused Preference of Multiple Objectives” Computational Statistics and Data Analysis 71 1178-1192
Lu, L., Anderson-Cook, C.M., and Robinson, T.J. (2011) “Optimization of Designed Experiments based on Multiple Criteria Utilizing a Pareto Frontier”, Technometrics, 53, 353-365.
Walsh, S.J. and Borkowski, J.J. (2022) “Generating exact optimal designs via particle swarm optimization: assessing efficacy and efficiency via case study”, Quality Engineering. https://doi.org/10.1080/08982112.2022.2127364.
Walsh, SJ and Borkowski, JJ. Improved G-optimal designs for small exact response surface scenarios: fast and efficient generation via particle swarm optimization. Mathematics: Special Issue Optimal Experimental Design and Statistical Modeling, November 13, 2022. https://doi.org/10.3390/math10224245
Zahran, A., Anderson-Cook, C.M. and Myers, R.H. (2003) “Fraction of Design Space to Assess the Prediction Capability of Response Surface Designs” Journal of Quality Technology 35 377-386.

## Slide 32: Backup

## Slide 33: Important Quantity definitions Objectives)
(ideal point)
(independent optimal design searches)
(feasible region)
(Pareto Dominance) Definition:
Given , we say is Pareto Dominant over , denoted
(Set of Pareto Front Designs)

## Slide 34: Response surface methodology (RSM) starting point
Vector expanding covariate vector
to assumed polynomial
Linear parameter vector:
partial derivatives of covariates and functions of
Aggregated Taylor Approximation Error
Confounded errors attributable to the measurement device and
Experimental repeatability
Linear Taylor Series Approximation
Design point Design Space
Non-linear Model

## Slide 35: Example and Notation: Second-order linear model, factors, design points
(1) Exact Design Matrix
(2) Second-order model in factors
(3) Model Vector
(4) Model Matrix
(5) Full Linear Model