Converting Digital Elevation Models into GRIDS and TINS for use in ArcView and ArcGIS

The following documentation outlines conversion steps for the following DEM and DTM formats for use in ArcView and ArcGIS:

- Digital Terrain Model (DTM) data from NRVIS

- Digital Elevation Model (DEM) data from NRVIS

- DEM data from DMTI

- Canadian Digital Elevation Data (CDED) from NRCan

The data from these sources come in point format.  The amount of detail in a GRID or TIN is a direct function of the number of sample points used in the original data source.  Thus, the more points used to create the GRID or TIN, the more detailed the image will be.  Furthermore, the more points used, the longer the processing time required to construct each GRID and TIN.

Instructions for importing each of the above DEMs into ArcView and ArcGIS are discussed by data type.  Note: DEMs and DTMs are synonymous.

Note:  Each of the images used in this document to illustrated the resulting GRID’s and TIN’s from the above sources are taken from the same area (Waterloo Area)

Converting Digital Terrain Model (DTM) data from NRVIS

File Format: *.shp

Convert to GRID in ArcView:

- Start a new view and turn on the Spatial Analyst and 3d Analyst extensions.

- Open the *.shp file of the area you want to view.

- In the Theme menu – Click Convert to GRID.

- Select the name and location of the new grid to be constructed.

- Select ‘SPOT’ as the attribute from which to derive the grid (Note: Alternate synonyms for ‘SPOT’ include ‘ELEV,’ ‘Z-Factor,’ ‘Height’ etc).

The conversion can take up to 15 minutes depending on the number of points in the shapefile.

When the conversion is complete, you will be asked to join the attribute table.  If you just want to view the GRID click no.  If you need the attribute for further analysis, click yes.  Note:  Joining the attribute table can take longer than the construction of the GRID itself.

Convert to TIN in ArcView

Note: You must have constructed a GRID before proceeding and you must have the Spatial Analyst and 3d Analyst extensions turned on.

- Click on the GRID in the viewer that you want to convert.

- Click on Convert to GRID from the Theme menu.

- Specify a filename for our new TIN and click OK.

- You will be prompted to specify a z-value tolerance.  This value represents the max plus/minus height that the output TIN can differ in relation to the center value of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

NRVIS DTM GRID using ArcView 	          NRVIS DTM TIN using ArcView

Converting to GRID in ArcGIS:

- Start ArcMap and turn on the Spatial Analyst menu that is located under the toolbar menu in the View pull down menu.

- Using the Spatial Analyst menu, go to Inverse Distance Weighted under the Interpolate to Raster menu.  (Note: There are a few choices for GRID conversion.  If you are unfamiliar with the workings of each, use Inverse Distance Weighted as it is a good all around choice).

- In the box that opens up—click on the folder to select the *.shp that you want to convert to a DEM.  On the right, your Height source is ‘SPOT’ and your Triangulate as: is ‘Mass Points.’ Leave the Tag Value Field as default.  Indicate the destination and name of the output GRID at the bottom and click Ok.

Converting to TIN in ArcGIS:

Note: You must have constructed a GRID before proceeding and you must have the Spatial Analyst and 3d Analyst extensions turned on.

- Click on the GRID in the viewer that you want to convert.

- Click on Convert to GRID from the Theme menu.

- Specify a filename for our new TIN and click OK.

- You will be prompted to specify a z-value tolerance.  This value represents the max plus/minus height that the output TIN can differ in relation to the center value of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

Note: Both of these conversions can take up to 30 minutes or longer depending on the number of input points.  Furthermore, draw time for the TIN can be upwards of 10 minutes.

NRVIS DTM GRID using ArcMap	          NRVIS DTM TIN using ArcMap

Converting Digital Elevation Model (DEM) data from NRVIS

File Formats: *.dem ; *.hdr – Header File ; *.htm – Metadata File

Converting to GRID in ArcView:

- Start a new view and turn on the Spatial Analyst and 3d Analyst extensions.

- Click Import Data Source under the File menu.

- Under the Select Import File Type menu that appears, select Binary Raster from the pull down menu.

- A new box will appear for the selection of the input DEM.  In the List of File Types on the bottom left, change to All file types.  In the window on the right, click the path where your DEM is located then click on the file with the *.dem extension and click Ok.

- Select a name and location for your new grid in the next window that appears and click Ok.

Converting to TIN in ArcView

Note: You must have constructed a GRID before proceeding and you must have the Spatial Analyst and 3d Analyst extensions turned on.

- Click on the GRID in the viewer that you want to convert.

- Click on Convert to GRID from the Theme menu.

- Specify a filename for our new TIN and click OK.

- You will be prompted to specify a z-value tolerance.  This value represents the max plus/minus height that the output TIN can differ in relation to the center value of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

NRVIS DEM GRID using ArcView	         NRVIS DEM TIN using ArcView

Converting to GRID in ArcGIS:

- Start ArcToolBox (This is a stand alone program that is found under the ArcGIS directory).

- Click Floating Point to GRID under the Import to Raster menu.

- Specify your input DEM and output raster then click OK.

- Start ArcMap and open new raster—Note: If prompted to build pyramids, click Yes.

Converting to TIN in ArcGIS:

- Using the 3d Analyst menu, go to Raster to TIN under the Convert menu.  In the box that opens up, select the input theme to convert.  The Z-tolerance can remain as the default.  Again, this value represents the max plus/minus height that the output TIN can differ in relation to the center of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

- The new TIN will automatically be added to the view when complete.

NRVIS DEM GRID using Arc Map	          NRVIS DEM TIN using ArcView

Converting DEM data from DMTI

File Formats: *.acs – ASCII File ; *.prj – Projection File

Converting to GRID in ArcView:

- Start a new view and turn on the Spatial Analyst and 3d Analyst extensions.

- Click on Import Data Set from the File menu.

- In the menu that appears choose ASCII Raster in the pull down menu.  Click Ok.

- Choose the file that you want to convert and the filename for the output GRID

- When prompted for Cell Values as Integers, click No.

- When the Grid is complete, you will be prompted to add the GRID to the view.

Converting to TIN in ArcView:

Note: You must have constructed a GRID before proceeding and you must have the Spatial Analyst and 3d Analyst extensions turned on.

- Click on the GRID in the viewer that you want to convert.

- Click on Convert to GRID from the Theme menu.

- Specify a filename for our new TIN and click OK.

- You will be prompted to specify a z-value tolerance.  This value represents the max plus/minus height that the output TIN can differ in relation to the center value of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

DTMI DEM GRID using ArcView	        DMTI DEM TIN using ArcView

Converting to GRID in ArcGIS:

- Start ArcToolBox.

- Click ASCII to GRID under the Import to Raster menu.

- Specify your input DEM and output raster.

- Check Floating Point and click OK.

- Start ArcMap and open new raster.

- When prompted to build pyramids, click Ok.

Converting to TIN in ArcGIS:

- Using the 3d Analyst menu, go to Raster to TIN under the Convert menu.  In the box that opens up, select the input theme to convert.  The Z-tolerance can remain as the default.  Again, this value represents the max plus/minus height that the output TIN can differ in relation to the center of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

- The new TIN will automatically be added to the view when complete.

DMTI DEM GRID using ArcMap	          DMTI DEM TIN using ArcMap

Converting Canadian Digital Elevation Data (CDED) from NRCan

File Format: *.dem

Converting to GRID in ArcView:

- Start a new view and turn on the Spatial Analyst and 3d Analyst extensions.

- Click on Import Data Set from the File menu.

- In the menu that appears choose USGS DEM in the pull down menu.

- When the Grid is complete, you will be prompted to add the GRID to the view.

Note:  If the GRID does not appear in your view, click on the GRID on the left then click Zoom to Themes in the View Menu.

Converting to TIN in ArcView:

Note: You must have constructed a GRID before proceeding and you must have the Spatial Analyst and 3d Analyst extensions turned on.

- Click on the GRID in the viewer that you want to convert.

- Click on Convert to GRID from the Theme menu.

- Specify a filename for our new TIN and click OK.

- You will be prompted to specify a z-value tolerance.  This value represents the max plus/minus height that the output TIN can differ in relation to the center value of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

CDED DEM GRID using ArcView	      CDED DEM TIN using ArcMap

Converting to GRID in ArcGIS:

- Start ArcToolBox.

- Click DEM to GRID under the Import to Raster menu.

- Specify your input DEM and output raster.

- Check Floating Point and click OK.

- Start ArcMap and open new raster.

Converting to TIN in ArcGIS:

- Using the 3d Analyst menu, go to Raster to TIN under the Convert menu.  In the box that opens up, select the input theme to convert.  The Z-tolerance can remain as the default.  Again, this value represents the max plus/minus height that the output TIN can differ in relation to the center of each cell from the input GRID (ArcView Help).  The default value is typically ok to use unless you are doing advanced analyses.

- The new TIN will automatically be added to the view when complete.

CDED DEM GRID using ArcMap	         CDED DEM TIN using ArcMap

Complied by: Christopher Close, June 26, 2003